## Slide 1
Quality Risk Management, ICH Q9(R1)
Training Slides
Preliminary Hazard Analysis (PHA)
International Council for Harmonisation of Technical Requirements
for Pharmaceuticals for Human Use

## Slide 2: Legal Notice
This presentation is protected by copyright and may, with the exception of the ICH logo, be used, reproduced, incorporated into other works, adapted, modified, translated or distributed under a public license provided that ICH's copyright in the presentation is acknowledged at all times. In case of any adaption, modification or translation of the presentation, reasonable steps must be taken to clearly label, demarcate or otherwise identify that changes were made to or based on the original presentation. Any impression that the adaption, modification or translation of the original presentation is endorsed or sponsored by the ICH must be avoided.
The presentation is provided "as is" without warranty of any kind. In no event shall the ICH or the authors of the original presentation be liable for any claim, damages or other liability arising from the use of the presentation.
The above-mentioned permissions do not apply to content supplied by third parties. Therefore, for documents where the copyright vests in a third party, permission for reproduction must be obtained from this copyright holder.​

## Slide 3: PHA in ICH Q9(R1)
ANNEX I: QUALITY RISK MANAGEMENT METHODS AND TOOLS
ICH Q9 (R1) states following about PHA:
I.7 Preliminary Hazard Analysis (PHA)
PHA is a tool of analysis based on applying prior experience or knowledge of a hazard or failure to identify future hazards, hazardous situations and events that might cause harm, as well as to estimate their probability of occurrence for a given activity, facility, product or system. The tool consists of: 1) the identification of the possibilities that the risk event happens, 2) the qualitative evaluation of the extent of possible injury or damage to health that could result, 3) a relative ranking of the hazard using a combination of severity and likelihood of occurrence, and 4) the identification of possible remedial measures.
Potential Areas of Use(s)
PHA might be useful when analyzing existing systems or prioritising hazards where circumstances prevent a more extensive technique from being used. It can be used for product, process and facility design as well as to evaluate the types of hazards for the general product type, then the product class, and finally the specific product. PHA is most commonly used early in the development of a project when there is little information on design details or operating procedures; thus, it will often be a precursor to further studies. Typically, hazards identified in the PHA are further assessed with other risk management tools such as those in this section.
3

## Slide 4: PHA Basics
What a typical PHA worksheet looks like:
*Note: Headers and layout may differ
Process/System: |  |  |  |  |  |  |  | 
Process Step/Function | Hazard | Harm | Severity | Hazardous Situation/Cause | Current Preventive Controls | Prob. Of Occur. | Risk | Recommendations / Actions
4
Notes: Example only

## Slide 5: PHA Strengths and Limitations:
Strengths: Early Identification of Hazards: PHA allows for the identification of hazards early in the development or design stage, which can lead to proactive risk management and prevention measures (Boeing, 2007). Structured Approach: PHA provides a structured method for evaluating potential hazards. It facilitates a systematic approach to identifying and analyzing risks, ensuring that important factors are not overlooked (American Institute of Chemical Engineers, 2006). Flexible and Scalable: PHA can be adapted to different industries and scales of projects, making it a versatile tool that can be applied across various sectors including aerospace, chemical manufacturing, and construction (International Organization for Standardization, ISO 31000). Facilitates Communication: The PHA process encourages collaboration and communication between various stakeholders, which can lead to better decision-making and risk management strategies (Heinrich, 1992).
Limitations:
Limited Depth of Analysis: As a preliminary tool, PHA does not provide a comprehensive analysis of all hazards and risks. It may miss detailed risk evaluations that more sophisticated methods (like Quantitative Risk Assessment) would provide (American Institute of Chemical Engineers, 2006). For combination of different tools see also ICH Q9 (R1) training slides “Combination of tools”
Dependence on Team Expertise: The effectiveness of a PHA is highly dependent on the expertise and experience of the team conducting it. A lack of knowledge or experience can lead to incomplete hazard identification (Hale & Hovden, 1998).
Snapshot in Time: PHA is often a snapshot of the project at a specific point in time. As projects evolve, new hazards may emerge that were not considered during the initial analysis which may not always be the case (Heinrich, 1992). This is particularly important when PHA is used as a precursor for other QRM tools.
5
Notes: Example only

## Slide 6: PHA Potential Areas of Use(s)
PHA may be used for…
analysing hazards and their related risks in existing systems
prioritising hazards for action
evaluating the types of hazards presented in products (e.g. type, class, etc...), processes and in facility design
PHA is frequently used early in the development of a process or product, when little information or experience may be available about that process or product.
PHA may be followed by additional risk assessments, using other quality risk management tools, which can aid in the design of further studies and in the identification of the required risk controls.
6

## Slide 7: PHA - Key Definitions
Hazard | Potential source of harm (ICH Q9(R1), ISO/IEC Guide 51)
Harm | Damage to health, including the damage that can occur from loss of product quality or availability (ICH Q9(R1))
Hazardous Situation or Event | Circumstances in which people, property or the environment are exposed to a hazard(s) (ISO 14971)
Severity | Measure of the possible consequences of a Hazard (ICH Q9(R1))
Probability | Extent to which an event is likely to occur (ISO/IEC Guide 73)
Risk | Combination of the probability of occurrence of harm and the severity of that harm (ISO 14971)
Note: See ICH Q9(R1) for the full citations/references for the above publications.
7

## Slide 8: PHA Execution
  The following are usually the main steps in a Preliminary Hazard Analysis:
  Identify the item or process step within the Product/Process/System under analysis. A risk question for the analysis may also be developed at this stage.
  Identify hazards associated with the various component/elements of the product/system, or with the processing steps. This can be done based on previous experience, a knowledge about sources of variability, deviations, complaints, accidents, literature, etc.)
  Determine the potential harms caused by the hazards, in terms of their potential impacts to product quality and/or patient safety.
  Identify the hazardous situations that would cause the hazards to result in such harms.
  Determine the controls that are in place to prevent the hazards from resulting in such harms.
  Evaluate the risk presented by each hazard.
  Make recommendations for, or identify, the required actions.
8

## Slide 9: PHA Execution - Risk Analysis
Risk Analysis in a PHA context consists of the qualitative and/or quantitative estimation of the risks associated with the identified hazards:
Score the Severity associated with the harms presented by the hazard or hazardous situation.
    What are the consequences of the hazard resulting in a harm (severity) to Product Quality/Patient Safety?
Score the Probability of Occurrence associated with the hazard or hazardous situation.
      Determine the probability of occurrence (or the frequency) that the hazard will lead to harm given the hazardous situation and taking into account the preventive controls.
    3. Estimate the Risk presented by the hazard. This is the combination of severity and probability (frequency) of harm
9

## Slide 10: PHA Execution - Risk Analysis cont’d
It is essential to identify the current prevention controls or mechanisms that are in place for the hazards and their associated potential harms:
  It is useful to document the current state of the system/process/design, before any additional risk reduction action is recommended/taken.
  To determine the assignment of probability of occurrence.
Prevention Controls: These relate to controls that can prevent the hazardous situation from occurring and therefore they serve to reduce its occurrence.
  The following are some prevention control categories:
    Design Controls: These relate to design aspects of the equipment, system or process that prevent the hazards or hazardous situations from occurring (e.g., process design elements such as alarms that put processing on hold, fit-for-use product inspection activities, etc.)
    Quality System Controls: These include aspects of the quality system such as procedures, batch records, training activities, etc., that may prevent hazards or hazardous situations from occurring
    Manufacturing Controls: These may include the validation or qualification of systems, equipment, processes, or personnel that provide evidence of operational effectiveness in preventing hazards or hazardous situations.
Note: At this stage of a PHA exercise, one should only consider the controls that are currently in place, not the controls that may be implemented in the future.
10

## Slide 11: PHA Execution - Risk Evaluation
This relates to determining Risk Acceptability.
Key activities here include:
  Evaluate the risks against predefined acceptability criteria.
  If a risk is determined to be acceptable, document the justification for its acceptance.
  If a risk is determined to be unacceptable, determine what can be done to reduce or eliminate the risk.
  Assess the appropriate balance between benefits, risks and the available resources.
  Identify recommended action.
  Do the implemented actions introduce any new risks?
11

## Slide 12
CASE STUDY:
Preliminary Hazard Analysis of a Packaging Process

## Slide 13
This case study presents a step-by-step approach for conducting a PHA on a packaging process in a multi-product facility.
The area of concern is the packaging of Injectable Product X on Packaging Line A.
Product X is a life-saving medicine used in emergency situations.
The PHA tool used in this case study involves scoring the severity and probability of occurrence for the hazards and harms in question and calculating their risk values.
The probability and severity scales used by the PHA tool are five-point ordinal scales, ranging from 2 to 10. Alternative scales could be used, as needed.
  See the ICH Q9(R1) training presentation titled "Subjectivity in Quality Risk Management Part II" for training content on risk rating scales.
This case study focusses on two identified hazards in one step of the packaging process of Product X. This is the vial labelling step. It demonstrates how to perform the PHA.
  Typically, a PHA would be more comprehensive, consisting of numerous identified hazards.
Note: This case study is not designed to provide training on how to rate and rank the risks associated with the two identified hazards; this is not the focus of the case study.
  The case study focusses on the essential steps of conducting a PHA exercise, and on the main principles to consider.
PHA Case Study - Introduction

## Slide 14: PHA Case Study - Initiating the PHA Process, Risk Question & Scope
It is useful to define a risk question for the PHA exercise, taking into account any pertinent assumptions that may be important.
  ICH Q9(R1) states that “when the risk in question is well defined, an appropriate QRM tool can be identified and the types of information needed to address the risk question will be more readily identifiable.”
  In this case study, the following risk question was defined:
    ‘What potential risks to product quality may arise during the packaging operations on Packaging Line A for Injectable Product X?’
It is important to define the scope of the PHA exercise (e.g., does it apply to the entire manufacturing process, or just selected parts of it, and is there a clearly defined boundary?
  In this case study, the scope of the PHA was the vial labelling step for the packaging of Product X on Line A.
  The boundary of the exercise was from step 6.1 in the master packaging batch record for product X to step 6.8, inclusive.

## Slide 15: PHA Case Study - the analysis worksheet
Process/System: Packaging Line A |  |  |  |  |  |  |  | 
Process Step/Function | Hazard | Harm | Severity | Cause | Current Controls | Prob. of Occur. | Risk | Recommendation / Action
Product X Packaging Process on Line A - Vial Labeling Step | Non labelled vials | Product cannot be identified and patients do not receive their medicine | 10 | Line speed too high, vial ejector mechanism fails | SOPs for machine set-up, operation, and troubleshooting Periodic equipment maintenance (Note: while there are procedural controls in place to prevent non-labelled vials getting packaged and released, no design controls are in place.) | 4 | 40 | Revisit line speed and re-qualify the narrower range. Re-code the line software to incorporate a maximum line speed.
 | Incorrectly labelled vial (wrong product strength) | Potential; Overdose/ Underdose | 10 | Label mix-up | Label and version number specified in bill of materials on batch record. Manual label checks prior to start of production. Manual In-process label checks. Manual QC label check at end of production. | 4 | 40 | Label camera system to be installed and qualified / validated.
 |  |  |  | Line clearance failure | Line clearance SOP, records of line clearance checks | 2 | 20 | Monitor effectiveness of existing controls
1. Identify the specific process or system to be risk assessed.
2. Identify the hazard based on process knowledge, previous experience, deviations, complaints, accidents, etc.
3. Identify the potential harm(s) caused by the hazard

## Slide 16: PHA Case Study – worksheet cont’d
Process/System: Packaging Line A |  |  |  |  |  |  |  | 
Process Step/Function | Hazard | Harm | Severity | Cause | Current Controls | Prob. of Occur. | Risk | Recommendation / Action
Product X Packaging Process on Line A - Vial Labeling Step | Non labelled vials | Product cannot be identified and patients do not receive their medicine | 10 | Line speed too high, vial ejector mechanism fails | SOPs for machine set-up, operation, and troubleshooting Periodic equipment maintenance (Note: while there are procedural controls in place to prevent non-labelled vials getting packaged and released, no design controls are in place.) | 4 | 40 | Revisit line speed and re-qualify the narrower range. Re-code the line software to incorporate a maximum line speed.
 | Incorrectly labelled vial (wrong product strength) | Potential; Overdose/ Underdose | 10 | Label mix-up | Label and version number specified in bill of materials on batch record. Manual label checks prior to start of production. Manual In-process label checks. Manual QC label check at end of production. | 4 | 40 | Label camera system to be installed and qualified / validated.
 |  |  |  | Line clearance failure | Line clearance SOP, records of line clearance checks | 2 | 20 | Monitor effectiveness of existing controls
The severity of harm (i.e., the hazard’s effect) is scored assuming the hazard/harm occurs. Note: The severity score is independent of the probability of occurrence of the hazard/harm.
The probability of occurrence is scored based on the hazard resulting in the harm, given the hazardous situation and the current controls that are in place.
The risk level is based on a combination of severity and probability of occurrence.
Determine recommendations to achieve to acceptable residual risk
Note: If a hazard has multiple harms or hazardous situations, score each individually to avoid blending score estimates

## Slide 17: Summary
PHA can be used to analyse processes, products, systems, etc., for hazards, to assess the risks presented by those hazards, and to prioritise the hazards for risk control.
PHA is often used where circumstances prevent a more extensive/rigorous QRM technique from being used.
It is frequently used early in the development of a process or product, when information and knowledge may be limited.
The case study in this presentation shows a stepwise procedure for performing a PHA, whereby the step or process of concern is identified, its potential hazards are identified and assessed for their potential harms, their root causes and their associated risk levels, taking into account the current controls that are in place.
In this way, a PHA helps to systematically identified risk mitigating actions for the hazards of concern.

## Slide 18: EWG Acknowledgment and Contact
Acknowledgement to the ICH Q9(R1) Expert Working Group (EWG)
For any questions, please contact the ICH Secretariat:
admin@ich.org